## Slide 1
Day 18 — Model Comparison & Mentor Review
All methods compared · Overfitting / failure analysis · Candidate shortlist · Next experiments
Sreetama Santra | IEM, Salt Lake, Kolkata
TIH IIT Guwahati | Mentor: T. Vamsikrishna | Group S2 | Week 3 — Day 18 | 2026-09-06
Models evaluated on: Dataset V1 frozen split · 8 features (Voltage, Current, Temp, Power, roll_mean_V, roll_mean_I, dV/dt, cc_cv_flag) · time_elapsed excluded (Day 16 overfitting finding)
Validation: Mixed7 from all 6 temperatures (272,565 rows)
XGBoost: best_iteration = 283 of 500 (early stopping triggered at round 303)
Remaining Charging Time model: not yet trained — pending Charge file pipeline completion
Slide 2: Full Comparison Table · Slide 3: Analysis & Shortlist
1 / 3

## Slide 2
Slide 2 | Full Method Comparison — SoC Estimation
All models trained on Dataset V1 frozen split · metrics on validation set · features without time_elapsed
SoC Estimation — Validation Set Metrics
Model | Train MAE | Val MAE | Val RMSE | Val R² | Overfit Gap | Status
Mean Predictor (null baseline) | — | 22.33% | 26.41% | −0.016 | N/A | Null
Linear Regression (9 features w/ time) | ~5.2% | 4.98% | 7.04% | 0.928 | ~0.2% | Baseline
Linear Regression (8 features, no time) | 3.10% | 3.31% | — | 0.972 | 0.21% | Baseline
RF with time_elapsed | 0.08% | 9.76% | 11.50% | 0.804 | 9.68% ⚠ | Overfits
RF without time_elapsed | ~2.0% | ~4.52% | ~5.8% | ~0.942 | ~2.52% | Acceptable
XGBoost (283 trees, no time) | 1.58% | 3.53% | 4.62% | 0.969 | 1.95% | Good
MLP Small — (64,32), no time | 1.75% | 2.49% | 3.32% | 0.983 | 0.74% | Good ✓
MLP Medium — (128,64,32), no time | 1.55% | 2.29% | 3.13% | 0.985 | 0.74% | Best ✓
Remaining Charging Time (RCT): not yet evaluated — Charge file preprocessing pipeline pending. Training planned for Days 19–21.
Literature benchmark: Kollmeyer 2020 DNN — RMSE < 1.5% · Chemali 2018 LSTM — MAE < 1.0% · Our MLP Medium MAE = 2.29% — within range for a feedforward network without recurrence
2 / 3

## Slide 3
Slide 3 | Analysis, Failure Patterns & Shortlisted Candidates
What the comparison reveals — where each model fails — what to do next
Key Findings from Comparison
RF with time_elapsed — severe overfitting (gap 9.68%)
Train MAE=0.08%, Val MAE=9.76%. Memorises session timeline. Fails on val files starting at different SoC levels. time_elapsed excluded from all subsequent models.
XGBoost — good but doesn't beat MLP (gap 1.95%)
Val MAE=3.53%, RMSE=4.62%, R²=0.969. Early stopping at iteration 283. Better than RF (no time) but worse than both MLP variants. Built-in regularisation works but the continuous SoC non-linearity favours the MLP architecture.
Linear Regression — surprisingly competitive baseline
Val MAE=3.31%, R²=0.972, zero overfitting. Fails at SoC extremes (0–20%: MAE=7.82%, 80–100%: MAE=6.35%). Good interpretability and speed. Retained as reference.
MLP Medium — best model, BEATS 3% target (gap 0.74%)
Val MAE=2.29%, RMSE=3.13%, R²=0.985. Overfit gap only 0.74%. Per-range: 0–20%=2.44%, 20–80%=2.07%, 80–100%=3.05%. Captures S-curve non-linearity that XGBoost and LR miss.
Shortlisted Candidates
#1
MLP Medium (128,64,32)
Val MAE=2.29% R²=0.985
Best accuracy, controlled overfitting.
Recommended for full-dataset retraining
and error analysis (EXP-004).
#2
XGBoost (283 trees)
Val MAE=3.53% R²=0.969
Fast inference, interpretable importance.
Recommended for XGBoost-Colab run on
full 6-temp dataset for fair comparison.
#3
Linear Regression
Val MAE=3.31% R²=0.972
Zero overfitting, fastest, most interpretable.
Retained as permanent baseline for
all future comparisons.
Data Limitations
• 40°C Mixed7: only 1,847 rows — anomalous
• −20°C: SoC span only 52.9%
• 0–20% SoC: sparse (7.9% of rows)
• RCT: not yet trained
3 / 3