## Slide 1
Day 21 — Best Candidate Review & Week 4 Direction
Week 3 summary · Baseline vs tuned · Ablation findings · Failures · Week 4 plan
Sreetama Santra | IEM, Salt Lake, Kolkata
TIH IIT Guwahati | Mentor: T. Vamsikrishna | Group S2 | Week 3 — Day 21 | 2026-09-09
Week 3 Work Completed:
• Day 15: Baseline — Mean predictor (MAE=22.33%) and Linear Regression (MAE=4.98%)
• Day 16: Ensemble — RF overfitting discovered (gap=9.68%), RF without time_elapsed (MAE=4.52%)
• Day 17: MLP Small (MAE=2.49%) and MLP Medium (MAE=2.29%) — beats 3% target
• Day 18: Comparison review — XGBoost MAE=3.53%, MLP Medium shortlisted as #1
• Day 19: Hyperparameter search — 9 configs, best EXP-H03 (256,128,64) MAE=2.31%
• Day 20: Ablation — Temperature is critical (+2.07%), failure zones identified
Slide 2: Baseline→Tuned · Slide 3: Ablation Findings · Slide 4: Successes & Failures · Slide 5: Week 4 Plan
1 / 5

## Slide 2
Slide 2 | Baseline → Tuned: Full Progression
All SoC models on Dataset V1 validation set · 8 features (no time_elapsed)
Model Progression — SoC Estimation (Validation Set)
Model | Train MAE | Val MAE | Val RMSE | Val R² | Overfit Gap | Status
Mean Predictor | — | 22.33% | 26.41% | −0.016 | N/A | Null floor
Linear Regression (no time) | 3.10% | 3.31% | — | 0.972 | 0.21% | Baseline
RF with time_elapsed | 0.08% | 9.76% | 11.50% | 0.804 | 9.68% ⚠ | Overfits
RF without time_elapsed | ~2.0% | ~4.52% | ~5.8% | ~0.942 | ~2.5% | Acceptable
XGBoost — 283 trees, no time | 1.58% | 3.53% | 4.62% | 0.969 | 1.95% | Good
MLP Small (64,32) | 1.75% | 2.49% | 3.32% | 0.983 | 0.74% | Good ✓
MLP Medium (128,64,32) | 1.55% | 2.29% | 3.13% | 0.985 | 0.74% | Best ✓
MLP Tuned EXP-H03 (256,128,64) | 1.52% | 2.31% | 3.07% | 0.986 | 0.79% | Final ✓
Improvement over baseline:
MAE: 22.33% → 2.31% (−20.02 pp, 89.7% reduction) · R²: −0.016 → 0.986
Literature benchmark (same dataset):
Kollmeyer 2020 DNN RMSE<1.5% · Chemali 2018 LSTM MAE<1.0% · Our MLP RMSE=3.07%
2 / 5

## Slide 3
Slide 3 | Project-Specific Study — Ablation & Robustness Findings
4 experiments run on Day 20 — where the model fails and why
EXP-A1: Error by SoC Range
SoC Range | MAE | Status
0–10% | 4.79% | Sparse data + S-curve ⚠
10–20% | 3.78% | Improving
20–40% | 4.27% | Mid-range
40–60% | 3.16% | Best ✓
60–80% | 3.23% | Good ✓
80–90% | 3.95% | Degrading
90–100% | 9.95% | Near-full-charge failure ✗
EXP-A2: Temperature Robustness
Temperature | MAE | R²
25°C | 2.03% | 0.990 ✓
10°C | 2.78% | 0.979 ✓
0°C | 4.00% | 0.961
−10°C | 5.52% | 0.912 ⚠
−20°C | 7.17% | 0.868 ✗
EXP-A3: Feature Ablation
Temperature is the ONLY critical feature: removing it raises MAE by +2.07%.
All other features are informationally redundant — removing any single one actually
slightly improves MAE (multicollinearity effect).
EXP-A4: Discharge Phase Analysis
Active discharge: MAE=6.02% (voltage drops rapidly under load)
Rest / low-current: MAE=3.97% (voltage near OCV, more predictable)
Transition: MAE=5.45%
Key Research Insight
Temperature is not just a context feature — it is the single most informative signal for cross-condition SoC estimation on the LG HG2 dataset. Without it, the model cannot distinguish between SoC levels at −20°C and 25°C even when voltage readings are identical.
3 / 5

## Slide 4
Slide 4 | Representative Successes, Failures & Remaining Weaknesses
What the best model does well — where it still struggles — what is fixable
Where the model succeeds
✓ Mid-SoC range (40–80%)
MAE=3.16–3.23%. The flat mid-range of the voltage-SoC S-curve is the most data-rich zone. Model learns this relationship well with abundant training examples.
✓ Room temperature (25°C)
MAE=2.03%, R²=0.990. Best individual condition. Clear voltage-SoC signal (r=0.965) and maximum data volume combine for near-literature-level performance.
✓ Rest-state prediction
MAE=3.97% at rest vs 6.02% during active discharge. When current is near zero, voltage is close to OCV and carries a strong predictable SoC signal.
✓ Generalisation (overfitting control)
Overfit gap=0.79%. Early stopping and Adam optimiser prevent the model from memorising training files. Consistent train-val performance across all 9 hyperparameter configs.
Where the model fails
✗ Near full charge — 90–100% SoC
MAE=9.95%. Sparse training data (only 4% of rows) + steep S-curve uptick. The model systematically under-predicts in this zone (negative residuals near 100% SoC).
✗ Extreme cold — −20°C
MAE=7.17%, R²=0.868. Voltage-SoC signal degrades to r=0.664. The battery's usable SoC span is only 52.9%, so the model never sees low SoC at this temperature.
✗ Active discharge transients
MAE=6.02% during active discharge vs 3.97% at rest. Rapid voltage drops under current pulses are hard to map to SoC — the model lags behind fast transients.
✗ Phase boundary transitions
The binned mean residual plot shows the model over-predicts at low SoC and under-predicts at high SoC — a systematic S-curve fitting bias that a feedforward MLP cannot fully resolve.
4 / 5

## Slide 5
Slide 5 | Week 4 Direction — Proposed Plan & Mentor Approval
Final model selection · error analysis · report · presentation
Proposed Week 4 Plan
Day 22
Full-Dataset Final Training
Retrain MLP EXP-H03 (256,128,64) on full 6-temperature training set (1.85M rows). Evaluate on frozen test set: Mixed8, UDDS, HWFET, LA92, US06.
Day 23
Final Error Analysis Report
Per-temperature and per-SoC-range breakdown on test set. Residual plots. Comparison table: LR vs XGBoost vs MLP on test set. Document unexpected errors.
Day 24
Peer Consolidation + Feedback
Compare test set results with S2 group. Document one peer finding and update hypotheses from actual test performance.
Day 25-26
Final Technical Report
Full internship report: problem, dataset, methods, experiments, results, ablation findings, limitations, future work. IEEE-style format.
Day 27
Final Presentation Preparation
Slide deck for final mentor presentation covering all 4 weeks. Include model demo / prediction walkthrough.
Day 28
Final Presentation & Submission
Present to mentor. Submit all deliverables, code, model artefacts, and experiment logs to GitHub and task portal.
Mentor Approval Needed
A1
Final model confirmed as MLP EXP-H03 (256,128,64)?
A2
Evaluate on full test set (Mixed8 + all drive cycles) on Day 22?
A3
Include XGBoost in final report as secondary candidate?
A4
Remaining Charging Time: include as future work only (Charge file pipeline not complete)?
A5
Is the 90–100% SoC failure zone acceptable or must it be resolved before Week 4?
A6
Week 4 report format: internship report only, or also a paper draft?
Mentor notes / corrections:
5 / 5