## Slide 1
Day 15 — Baseline Modelling & Mentor Review
Mean Predictor · Linear Regression · Per-Temperature Results · Modelling Direction
Sreetama Santra | IEM, Salt Lake, Kolkata
TIH IIT Guwahati | Mentor: T. Vamsikrishna | Group S2 | Week 3 — Day 15 | 2026-09-03
Context:
Dataset V1 frozen (Day 12). 9 features confirmed (Day 13). 1,849,732 training rows · 272,565 validation rows
Frozen split: Mixed1–6 (train), Mixed7 (val), Mixed8 + drive cycles (test) · Scaler fitted on training only
Metrics: MAE, RMSE, R² · Evaluated per-temperature and per-SoC-range
Slide 2: Results Summary · Slide 3: Per-Temperature · Slide 4: Key Plots · Slide 5: Modelling Direction
1 / 5

## Slide 2
Slide 2 | Baseline Results Summary
Both baselines trained and evaluated on frozen Dataset V1 split
Validation Set Metrics
Null Baseline
Mean Predictor
MAE: 22.33%
RMSE: 26.41%
R²: −0.016
Predicts the training mean SoC (53.4%) for every row regardless of input. Represents the absolute performance floor — any real model must beat this.
Baseline Model
Linear Regression
MAE: 4.98%
RMSE: 7.04%
R²: 0.928
Fits a single hyperplane through the 9-feature space. Explains 92.8% of variance in SoC. MAE = 4.98% is good for a linear model but exceeds our 3% target.
Week 3 Goal
Target (RF / XGBoost)
MAE: < 3.0%
RMSE: < 4.0%
R²: > 0.96
Expected from gradient boosting / ensemble methods based on literature. Kollmeyer 2020 DNN achieved < 1.5% RMSE on this exact dataset.
Linear Regression reduces MAE by 17.35% vs mean baseline (77.6% relative reduction). R² = 0.928 confirms strong linear signal but MAE = 4.98% still exceeds the 3% target → RF and XGBoost are needed.
2 / 5

## Slide 3
Slide 3 | Per-Temperature & Per-SoC-Range Results
Linear Regression — identifying where the model fails
MAE by Temperature (Validation)
Temperature | n rows | MAE | R²
40°C | 1,847 | 6.00% | −10.60 ⚠
25°C | 67,234 | 3.97% | 0.963 ✓
10°C | 63,324 | 2.93% | 0.981 ✓
0°C | 55,539 | 3.96% | 0.968 ✓
−10°C | 49,939 | 5.39% | 0.932 ✓
−20°C | 34,682 | 11.67% | 0.705 ✗
MAE by SoC Range (Validation)
SoC Range | n rows | MAE | Note
0 – 20% | 49,381 | 7.82% | Sparse + non-linear ✗
20 – 80% | 181,652 | 3.90% | Best performance ✓
80 – 100% | 41,517 | 6.35% | S-curve uptick ✗
Key Observations
40°C anomaly:
R²=−10.60 because Mixed7 at 40°C has only 1,847 rows — the short-session files we flagged in Day 7. Not representative.
−20°C worst:
MAE = 11.67% — voltage-SoC correlation r=0.664 at −20°C. Linear model cannot capture the compressed, noisy signal.
10°C best:
MAE = 2.93% — only temperature that already beats the 3% target with a linear model.
Low SoC worst:
MAE = 7.82% in 0–20% range. Sparse data (7.9% of rows) + steep S-curve = linear model failure zone.
3 / 5

## Slide 4
Slide 4 | Baseline Prediction Plots
From notebook — 5000-point sample of validation set
Plot 1 — Actual vs Predicted (Validation, 5000 sample)
Mean Baseline (left panel): flat horizontal line at 53.4% SoC. Predicts same value for every input. Perfect prediction line (red dashes) shows how far this is from correct.
Linear Regression (right panel): points cluster around the diagonal but with visible scatter. Over-prediction at low SoC (0–20%) and under-prediction at high SoC (80–100%) confirm the model misses the S-curve at the edges.
Plot 2 — Residuals (Linear Regression)
Left panel (residual vs actual SoC): systematic pattern — positive residuals at low SoC (over-predicts) and negative residuals at high SoC (under-predicts). Classic sign of a linear model fitting a non-linear curve. The error is NOT random — it has structure that a non-linear model can capture.
Right panel (residual distribution): approximately normal, centred near zero (mean residual = 0.20%), confirming no systematic bias in the overall prediction. The spread (±15–20%) confirms the wide error range that justifies moving to Random Forest.
4 / 5

## Slide 5
Slide 5 | Modelling Direction & Mentor Confirmation
Next steps based on baseline results
What the Baseline Tells Us
Linear model is viable in the mid-SoC range
MAE = 3.90% in the 20–80% SoC range is close to our 3% target. The linear relationship is strongest here — voltage changes gradually and predictably.
Non-linear model is essential at the extremes
MAE = 7.82% at 0–20% SoC and 6.35% at 80–100% SoC. The residual plot shows a clear systematic pattern — not random noise. Random Forest and XGBoost can capture this.
Cold temperature performance is the hardest challenge
MAE = 11.67% at −20°C. The voltage-SoC correlation drops to r=0.664 at −20°C. A model that trains across all 6 temperatures and uses non-linear splits will handle this better.
40°C validation anomaly needs clarification
R² = −10.60 at 40°C with only 1,847 validation rows. The Mixed7 at 40°C file is unusually short. This is a data quality flag, not a model failure.
Week 3 Modelling Plan
Day 16
Random Forest
n_estimators=100, feature importance, per-temp evaluation
Day 17
XGBoost
n_estimators=500, early stopping on val RMSE, regularisation
Day 18
Mentor Review 5
Comparison table: LR vs RF vs XGBoost, all metrics
Day 19–21
Error Analysis
Residuals per SoC range, temp generalisation study (EXP-004)
Mentor Confirmation Needed:
1. Proceed with RF and XGBoost as primary next models?
2. Investigate 40°C Mixed7 short-file anomaly before test evaluation?
5 / 5