## Slide 1
Week 2 — Day 9 | Data Quality Findings & Cleaning Proposal
Mentor Review 3 · Based on actual audit of 364,168 valid rows across 6 temperature conditions
1
Dataset audited: LG HG2 18650 | 208 CSV files | 6 temperatures | 364,168 valid TABLE rows (after PAU filter) | 0 random missing values in any sensor column
Missing Values — Clean
• 0 NaN in Voltage, Current, Temperature, Capacity after PAU filter
• 1 unit-row artifact per file — fixed by drop(index=0) on load
• No sensor dropout detected across any of the 208 files
Outliers — Keep
• 5,373 IQR outliers in Voltage (1.48%) — valid extreme SoC readings near 2.8V at −20°C and 4.2V at full charge
• Removing them would eliminate critical low/high SoC data from the model
• Rule: Use physical bounds only (2.5V–4.3V). No IQR-based removal.
Duplicates — Keep
• 21,654 exact duplicates (5.9%) — valid rest-state readings between drive cycles
• 74,253 near-duplicates V,I,T match (20.4%) — capacity still increments each row
• Rule: Do NOT deduplicate. These rows carry SoC continuity information.
PAU Rows — Remove
• Exactly 6,001 PAU rows per Mixed1 file across all 6 temperatures
• PAU = tester paused. Readings are rest-state, not representative of active driving
• Rule: Filter Status = PAU before any EDA, feature engineering, or model training.
Temperature Self-Heating (Key Finding)
Battery self-heats under load by up to 4.73°C at −20°C. The measured Temperature column deviates from folder nominal by up to ±4°C. Must use measured Temperature as input feature — never the folder name.
SoC Coverage Drops at Cold Temps
SoC span: 86.3% at 25°C but only 52.9% at −20°C. Models trained on 25°C data will not have seen the full SoC range at cold temperatures. Per-temperature evaluation is essential.

## Slide 2
Proposed Cleaning Plan & Split Logic
10 rules — 4 active cleaning steps and 6 architectural constraints
2
Active Cleaning Rules (do these)
R1
Drop unit-row at index 0 after header parse
Unit descriptor row (V, A, °C, Ah) causes all sensor columns to parse as object dtype. Must be removed before numeric conversion.
R2
Filter Status = PAU rows
PAU = tester paused. 6,001 rows per Mixed1 file. Readings not representative of active drive cycle behavior.
R3
Force numeric dtype on all sensor columns
pd.to_numeric(errors='coerce') ensures consistent float dtype. Silent failures in arithmetic are prevented.
R7
Exclude Charge files with fewer than 500 rows
Charge1 at 25°C has only 131 rows — CV tail only. Too few rows for reliable Remaining Charging Time label derivation.
Architectural Constraints (don't violate these)
R4
Do NOT remove IQR voltage outliers
5,373 outliers are valid extreme-SoC readings. Removing them deletes critical data from the model's training distribution.
R5
Do NOT deduplicate rows
20.4% near-duplicates are valid rest-state sensor readings. Capacity column still increments — these rows are needed for SoC continuity.
R6
Use measured Temperature — not folder name
Self-heating under load means actual temperature deviates up to 4.73°C from nominal. Folder name is inaccurate as a feature.
R8
Split by file — never by row
Row-level splitting destroys temporal order and allows future sensor readings into the training set (leakage).
R9
Fit scaler on training data only
Fitting on the full dataset leaks test statistics into the scaler and inflates test performance.
R10
Compute rolling features within each file
Rolling across file boundaries introduces data from one session into another — cross-file temporal leakage.

## Slide 3
Split Logic, Open Questions & Mentor Corrections
Proposed train/val/test split and items for mentor confirmation
3
Proposed Train / Validation / Test Split
Training
• Mixed1–6 from all 6 temperature folders
• Charge1–12 from all 6 temperatures
• Random mixed drive cycles cover diverse SoC trajectories. Charge files provide CC-CV data for Remaining Charging Time target.
Validation
• Mixed7 from all 6 temperature folders
• Charge13–14 from all 6 temperatures
• Same cycle type as training but different session. Used only for hyperparameter tuning and early stopping — never for final model selection.
Test
• Mixed8, UDDS, HWFET, LA92, US06 from all 6 temps
• Charge15–16 from all 6 temperatures
• Standard drive cycles are completely unseen during training. Tests generalization to real-world EV usage patterns.
Rule:
Every file stays entirely in one split. No row shuffling. No cross-file rolling. Scaler fit on training files only.
Questions for Mentor + Corrections
• Q1 — SoC derivation: per segment or continuous?
• Q2 — Q_nominal: temperature-specific or fixed 3.0 Ah?
• Q3 — Split: Mixed1-6 train, Mixed7 val, Mixed8+drive test?
• Q4 — Charge files under 500 rows: exclude or keep?
• Q5 — Do NOT remove IQR voltage outliers: confirmed?
• Q6 — Acceptable SoC MAE threshold for this project?
Mentor corrections:
________________________________ ________________________________ ________________________________